## Slide 1
AI Platform
Enterprise Deployment & Load Test Report
2-Node Kubernetes Cluster | Dify + code-server + litellm + Ollama
June 13, 2026

## Slide 2
Project Overview
AI Platform Enterprise Report | June 2026
Dify Platform
AI application platform
API + Web + Worker + Plugin Daemon
code-server
Browser-based VS Code IDE
20 pods, 2000 concurrent users
litellm
LLM proxy gateway
11 pods, 13 Ollama models
Open-WebUI
Chat interface
Connected to litellm
Ollama
LLM runtime engine
Master + Worker, CPU-only
Monitoring
Prometheus + Grafana
12 ServiceMonitors, 38+ Rules

## Slide 3
Architecture Overview
AI Platform Enterprise Report | June 2026
2-Node Kubernetes Cluster
k8s-master (16 CPU / 64 GB)
• ollama-master (15 CPU)
• Control plane components
• ingress-nginx
• Rancher
k8s-worker1 (32 CPU / 128 GB)
• ollama-worker (13 models)
• code-server (20 pods)
• litellm (11 pods)
• Dify (API/Web/Worker)
• PostgreSQL, Redis, Weaviate
Ingress (nginx NodePort)
code-server :32231 | litellm :30083 | Dify Web :30080 | Open-WebUI :30084 | Grafana :30082
No GPU available — all LLM inference runs on CPU

## Slide 4
Issues Identified & Resolved
AI Platform Enterprise Report | June 2026
code-server 404
Ingress only routed requests with Host header
Added catch-all ingress rule
✓ FIXED
Rancher Login
Password lost / incorrect
Reset to Rancher@2026
✓ FIXED
litellm Models
Config referenced non-existent models
Updated with all 13 actual ollama models
✓ FIXED
Ingress Rate Limit
limit-rps=30 capped all traffic
Removed rate limits → 88.6%→0% failures
✓ FIXED
Pod Scheduling
CPU requests too high for scaling
Reduced requests (2→500m, 1→200m)
✓ FIXED
No GPU
All LLM inference on CPU
Identified as critical gap for enterprise scale
✗ NEEDS GPU

## Slide 5
Code-Server Load Test — 2,000 Users
AI Platform Enterprise Report | June 2026
PASSED
0% service failures — all errors are incorrect test paths (404)
19,595
Total Requests
0%
Service Failures
145.7
Peak RPS
20
Pods Deployed
Endpoint Performance
GET /healthz
4,551
0%
10ms
PASS
GET /login
2,000
0%
9.1s
PASS
POST /login
2,000
0%
8.0s
PASS
GET / (workspace)
5,556
0%
56s
PASS

## Slide 6
LLM Services Load Test — 5,000 Users
AI Platform Enterprise Report | June 2026
DEGRADED — CPU Bottleneck
62.6% failure rate — chat/embeddings fail completely on CPU-only inference
81,429
Total Requests
62.6%
Failure Rate
371.4
Peak RPS
11
Pods Deployed
Endpoint Performance
GET /health/readiness
29,758
41.6%
21.6s
DEGRADED
GET /v1/models
22,317
41.4%
21.8s
DEGRADED
POST /v1/chat (7b)
14,784
100%
37.9s
FAIL
POST /v1/chat (14b)
7,353
100%
75.5s
FAIL
POST /v1/embeddings
4,308
99.98%
24.1s
FAIL

## Slide 7
Bottleneck Analysis
AI Platform Enterprise Report | June 2026
Ingress Rate Limiting
FIXED
limit-rps=30 capped code-server to 30 req/s. Removed → 0% failures.
CPU-Only LLM Inference
UNRESOLVED
No GPU. Chat takes 30-120s on CPU. 5000 concurrent impossible.
Master Node CPU Saturation
MITIGATED
ollama-master uses 15/16 cores. Reduced pod CPU requests.
Pod Resource Requests
FIXED
Original 2 CPU/pod prevented scaling. Reduced to 500m → 20 pods.
Static Asset Paths
TEST ISSUE
Test used wrong paths. 404 errors are test artifacts, not service failures.

## Slide 8
Scaling Actions Taken
AI Platform Enterprise Report | June 2026
Service
Replicas
CPU Request
Result
code-server
5 → 20 pods
2 CPU → 500m
2000 users supported
litellm
3 → 11 pods
1 CPU → 200m
5000 users attempted
dify-api
1 → 5 pods
unchanged
Platform stability
dify-web
3 → 5 pods
unchanged
Platform stability
dify-worker
1 → 5 pods
unchanged
Background tasks
Ingress
Rate limits removed
30→unlimited RPS
Eliminated bottleneck

## Slide 9
Recommendations
AI Platform Enterprise Report | June 2026
IMMEDIATE
Add GPU Infrastructure
2x A100 or 4x A10 GPUs for LLM inference — single most impactful improvement
IMMEDIATE
Offload ollama-master
Move from control plane to dedicated worker to free master CPU
SHORT-TERM
Configure HPA
HorizontalPodAutoscaler with working metrics for auto-scaling
SHORT-TERM
Smart Rate Limiting
Per-user/IP rate limits instead of global caps
SHORT-TERM
Add Worker Node
Third node for load distribution and scaling headroom
LONG-TERM
CDN for Static Assets
Offload code-server JS/CSS to CDN for faster loads
LONG-TERM
Model Response Cache
Redis cache for frequent LLM completions
LONG-TERM
Multi-Region Deployment
Geographic distribution for DR and latency

## Slide 10
Summary & Next Steps
AI Platform Enterprise Report | June 2026
What Went Well
✓ Code-server handles 2000 users
✓ All critical bugs fixed
✓ 20+ services deployed
✓ Full monitoring stack
✓ Ingress bottleneck resolved
✓ 5 issues identified & fixed
What Needs Work
✗ LLM services need GPU
✗ Master node CPU saturated
✗ No auto-scaling (HPA broken)
✗ Static asset paths incorrect
✗ No CDN for static content
Next Steps
1. Procure GPU hardware (2x A100 80GB minimum)
2. Add third worker node for load distribution
3. Configure HPA with proper metrics for all services
4. Implement per-user rate limiting strategy
5. Set up CDN for code-server static assets
6. Move ollama-master off control plane node
7. Schedule follow-up load test with GPU infrastructure

## Slide 11
Key Metrics Dashboard
AI Platform Enterprise Report | June 2026
2,000
Code-Server Users
0%
Service Failures
5,000
LLM Users Tested
62.6%
LLM Failure Rate
20
Code-Server Pods
11
Litellm Pods
13
Ollama Models
0
GPUs Available
Cluster Resources
Master: 16 CPU / 64 GB (96% CPU used) | Worker: 32 CPU / 128 GB (1% CPU, 43% mem)
Rancher: https://10.167.2.175 (admin / Rancher@2026) | Grafana: http://10.167.2.175:30082